|  | INTERNATIONAL AMATEUR RADIO UNION REGION 3 B a n d p l a n |  |
| --- | --- | --- |

1.8 MHz

3.5 MHz

Note:   Where the total band available nationally is 100 kHz or less, phone operation
may commence at 3.525 MHz.

7 MHz

10 MHz

14 MHz

Note:   Considering the dramatic increase in data mode usage on the 20 meter band, it is recommended that the sub-band for these classes of signals be 14.070 MHz to 14.112 MHz (with +/- 500 Hz at 14.100 MHz for beacons), and within that data sub-band the current practices of traditional data modes may continue up to 14.095 MHz with 14.095 to 14.112 MHz being reserved for other data modes including Packet.

18 MHz

21 MHz

24 MHz

28 MHz

50 MHz

144 MHz

430 MHz

1,240 MHz

Bands above 1300 MHz:

Societies should consult with the amateur satellite community for proposed satellite operating frequencies before deciding local bandplans above 1300 MHz.

The Basic Principles Underlying the IARU Region 3 Bandplan:

(1) In all cases of conflict between a bandplan and the national regulations of a country, the latter shall prevail.

(2) Nothing in these bandplans shall be construed as prohibiting different national arrangements, provided that harmful interference is not caused to stations in countries operating in accordance with the regional bandplan.

(3) Notwithstanding item 2 above, Member Societies of IARU Region 3 are strongly urged to use these regional bandplans as a basis for their national bandplans.

[Legends]

NB:	Narrow band modes including CW, RTTY, Packet and modes with similar bandwidth not exceeding 2 kHz.

Phone:	Phone operation includes SSTV, FAX and modes with similar bandwidth not exceeding 2 kHz.

WB:	Wide band modes including FM.

Satellite:	This segment should be kept clear of other operating modes.

EME:	Earth-Moon-Earth, Meteor Scatter, Auroral Scatter and other weak-signal.

Secondary:	At 7.1 to 7.3 MHz, amateur stations shall not cause harmful interference to stations of the Broadcasting Service.

____________________

# Text boxes

CW

Phone Operation

1.840

1.8

2.0

1.830

1.834

RTTY

DX

CW

DX

3.775

3.510

3.9

3.5

3.535

Phone Operation

CW

Secondary

7.040

NB

7.025

7.030

7.3

Phone

DX

3.800

7.1

Phone Operation

CW

7.0

NB

14.23

( 5 kHz
is recommended
for SSTV

10.14

10.10

Secondary

14.1127.040

NB

14.0

18.100

10.157.3

NB

CW

NB

14.070

14.1

( 500 Hz
guard band
for beacons

14.35

Phone Operation

CW

18.068

18.168

NB

18.110

International Beacon

CW

Phone

NB

21.34

( 5 kHz
is recommended
for SSTV

21.0

21.12540

24.930

International Beacon

21.070

21.15

( 500 Hz
guard band
for beacons

21.45

Phone Operation

CW

24.99

Phone

24.920

24.89

NB

CW

NB

28.68 ( 5 kHz
is recommended
for SSTV

28.0

28.150

28.050

28.3

29.7

Phone Operation

CW

WB

Satellite

29.510

29.3

28.2

28.190

Beacons

EME

54

Phone and WB

50.5

50

Beacons

CW

148

Satellite

144.035

144

145.8

146

438

1,296

EME

450

Satellite

431.9

430

432.240

435

1,270

1,297

EME

1,3000

Satellite

1,260

1,240